|  | Model Name：120 Meters HD Infrared Network High-speed Dome Model No：VL-SD01 Resolution：960P Infrared Distant：Distinguish Facial Feature in 120 meters |
| --- | --- |
|  | Specifications： 1、12 high-efficient Array infrared lamps, low power, can distinguish Facial Feature in 120 meters distance 2、Infrared lights auto open high beam or low beam according to the camera focus, to make the images to an ideal status. 3、Aluminum alloy shell with good heat radiation, to make it more stabilized and longer life. In-built anti-surge and lightning protection device 4、Aluminum wall-mount bracket, All-weather environment design, prevent the rain 5、 Support for the latest Onvif2.2, can be connected with the NVR of Haikang, Dahua, and etc. |
| Telecamera Parameters | CMOS | 1/3″Panasonic CMOS |
|  | Effective Pixels | 1.30MP(1280*960) |
|  | Horizontal Resolution | ≥900 TV lines |
|  | Video Format | 25fps@1280*960;30fps@1280*960 25fps@1280*720;30fps@1280*720 25fps@720*480;30fps@720*480 25fps@288*192;30fps@288*192 |
|  | Lowest Illumination | 0.5 Lux@F1.6(color）；0.09 Lux@1.6(black and white）；Infrared OLux |
|  | Power optical | 18 times，auto focus |
|  | Focal Length | 4.5 ~8.1mm |
|  | Angular | 55.4°~2.9° |
|  | Day and Night Mode | Auto IR-CUT Switch |
| Console Parameters | Rotate Speed | Horizon 0.1°~90°/second； Vertical 0.1°-40°/second |
|  | Preset Speed | Horizon 90°/second; Vertical 40°/second |
|  | Rotate Angular | Horizon 0°~360° rotation；Vertical 0°~90° auto 180° rolling over |
|  | Two point A-B Scan | Random Set |
|  | Speed of A-B Scan | Three class of speed to adjustable |
|  | Patrol Group | 8 Groups（8 presetting bits for each group） |
|  | Presetting Point | 128 |
|  | Electric action | Support |
|  | Guard Position | Support |
| Infrared Lamp | Infrared Lamp | Ф22=12 high-efficient Array infrared lamp, can distinguish Facial Feature in 120 meters distance |
|  | Auto Control Infrared Lamp | According to the focal length, auto switch to Infrared Lamp/Manual/high beam/low Beam during the night |
| Video Audio Alarm | Video Coding | H .264.;MPEG4 |
|  | Video Stream | Major：960P，720P Minor：D1，CIF |
|  | Image Resolution | 1280*960 |
|  | Rate Audio | 64K bps |
|  | Voice Intercom | Support |
|  | User Administration | Support Maximum users，Multi-level User Permission Administration |
|  | TCP/ | TCP/IP,HTTP,DDNS,PPOE,NIP,FTP,RTSP,RTP |
| Network Coding | Access Protocol | Onvif Standard |
|  | Net Interface | 1 route 10/100 Base internet，RJ45 interface |
|  | Remote Feature | Support Remote Set, Remote Update |
|  | Web Service | In-built Webserver Server, support IE brower |
|  | Network bandwidth | 64 kbps-12Wbps, Multi - level dynamic adjustable |
| Product Structure | Size | 7 inches |
|  | Shell Materials | Aluminum alloy |
|  | Framework Materials | Aluminum alloy |
|  | Engineer Room Material | Aluminum alloy |
|  | Input voltage | DC12V5A |
|  | Power | 40W |
|  | Operation Temperature | -25°C~70°C |
|  | Installation Method | Wall mounting or lifting mounting(standard lifting mounting) |
| Product Package | Package Size | 300mm×300mm×480mm |
|  | Package Gross Weight | 5.0Kg |