VL-H01

Feature

- 1/4" 1.0 Megapixel CMOS Sensor，Max image Resolution 1280*720@25fps

- H.264 Main Profile @ level 5.0 coding, Real time H.264 dual-stream encoding, resolution, frame rate, bit rate adjustable

- Support Color/BW mode converting, IR-CUT Filter

- Support Two-way Audio (Built-in MIC)

- auto-retrieve function and auto-connection network

- Built-in Pan/tilt,horizontally 355°,vertically 120°

- Support the SD card record, multiple record mode(Timed record, Motion Detection Record, Alarm Record), and support push the video to your smart phone when motion detected

- Support Plug-and-Play, including PC surveillance software and mobile phone client, remote network surveillance so easy

- Integrated ONVIF standard, Compatibility with third-party ONVIF platform software

Specifications

| Model | VL-H01 |
| --- | --- |
| Hardware |
| Processor | HI3518C |
| Sensor | 1/4" 1.0 Megapixel CMOS Sensor |
| Lens | 3.6mm Fixed Lens |
| IR LED | 12 IR Leds, IR Distance 5~10m |
| Day/Night | IR CUT filter |
| Min. Illumination | 0.5lux; 0 lux with IR on |
| Max S/N Ratio | 50dB |
| Video |
| Compression | H.264 |
| image | main stream: 1280x720@1-25fps sub stream: 640x360@1-25fps 320x180@1-25fps |
| Bit Rate | 128~4096kbps, Supports CBR/VBR |
| Image Control | Hue, saturation, brightness, contrast, exposure |
| Auto Image Control | AE, AWB |
| Audio |
| Compression | G.711-A |
| Bit Rate | 64kbps/128kbps |
| Talkback | support |
| Network |
| Protocol | TCP/IP, HTTP, DHCP, DNS, DDNS, RTP, RTSP, PPPoE, SMTP, NTP, SNMP, FTP, UPNP |
| Compliance | ONVIF 2.1(1.02 backward compatible) |
| PC Client and Browser | ISS, IE6.0 and above, Google Chrome, firefox |
| Mobile phone | Iphone, ipad, Android |
| WIFI | support |
| Wireless LAN | IEEE802.11n Standard |
| WIFI Encryption | WAP, WAP2 |
| Interface |
| Audio Input | Built-in MIC |
| Audio Output | 1 CH 3.5mm audio output interface |
| Alarm Input | 1 CH alarm input interface |
| Alarm Output | 1 CH alarm output interface |
| LAN | 1 RJ45 10M/100M Ethernet port |
| Wireless | 1 CH SMA antenna interface |
| Storage Interface | Micro SD (TF) Card slot, SD 2.0 standard, maximum 32GB |
| Reset Button | Built-in reset button |
| General |
| Working Temperature | -10℃~ +55℃ |
| Working Humidity | 0% - 90% |
| Power Supply | DC 5V/2A |
| Power Consumption | Max 8W |
| Dimensions | 103*108*125mm |
| Weight | 500g |
| Approvals | CE , FCC, RoHS |