Specification

| Model No. | VL-04NA87 |
| --- | --- |
| System | Video Compression Format | H.264 |
|  | Main Processor | HI3520D V200 + NVP1918C/6114 |
|  | Video System | NTSC / PAL |
|  | Operation System | Embedded Linux |
|  | AHD Signal System | AHD-L (960H) / AHD-M (720P) (Analog High Definition) |
| Video | Video Input | 4CH BNC |
|  | Video Output | 1 x VGA / 1 x HDMI (1920*1080) |
|  | Video Distance | 75-3 cable up to 500 Meters Transmission |
| Audio | Audio Input | 4CH RCA |
|  | Audio Output | 1CH RCA |
|  | Bidirectional Talk | YES |
| Recording | Recording Channel | 4CH 720P Real Time 4CH 960H Real Time |
|  | Resolution | NTSC - D1 (704 x 480) / 960H (960 x 480) / 720P (1280 x 720) |
|  |  | PAL - D1 (704 x 576) / 960H (960 x 576) / 720P (1280 x 720) |
|  | Frame Rate | NTSC 30fps / PAL 25fps |
|  | Recording Mode | Manual / Alarm / Motion Detection / Continuous |
| Playback | Playback Channel | 1CH 720P Real Time + 3CH 720P Non-Real Time 4CH 960H Real Time |
|  | Search Mode | Time / Date / Alarm / Motion Detection / Exact Search |
|  | Playback Mode | Normal Play / Fast Forward / Fast Rewind / Frame by Frame |
|  | Playback Software | General H.264 Player V1.7.0. |
| Alarm | Alarm Input | N/A |
|  | Alarm Output | N/A |
| Storage | HDD Interface | 2 x SATA Fixed HDD |
|  | Capability | SATA HDD up to 4TB each |
| Backup | USB Disk | 3 x USB 2.0 port |
|  | SNAP Image | NO |
|  | Backup Format | H.264 (only for Playback Software - General H.264 Player V1.7.0.) |
|  | Backup Mode | Network download / Flash USB / movable HDD/SATA HDD / DVD-RW |
| PTZ | PTZ | 1 x RS485 |
|  | Protocol | PELCO-P / PELCO-D / HY / NEON / PANASONIC / SAMSUNG / PHILIPS / SANLI / SANTACHI / SHARP / SONY / YAAN |
| Network | Interface | RJ45 port / 10M / 100M / 1,000Mbps Ethernet |
|  | Protocol | TCP/IP, DHCP, DDNS, DNS, PPPoE, UPNP, NTP, SMTP |
|  | CMS Program | General_CMS_Eng_V3.0.7.7.T (up to 500 Video channels Platform) |
|  | Mobile Phone Support | iPhone / iPad, Android, BlackBerry, Symbian, Windows Mobile Pro |
|  | Computer System Support | Windows 2000, XP, Vista, 7, 8 / Mac OS x 10.6/10.7 |
|  | Compatible Browser | Google Chrome, Internet Explorer (IE11), Mozilla Firefox, Safari (Mac) |
|  | 3G/WIFI | 3G/WIFI USB Dongle (Plug-and-Play) |
|  | Free DDNS (P2P) | P2P Function via iCloud server (http://www.xmeye.net) |
|  | IP Camera Protocol | ONVIF 2.3 Version Platform Protocol (IP Camera) |
|  | Channel Type (Digital Menu) | 4CH 720P AHD Camera 4CH 960H Analog Camera 2CH 720P AHD Camera + 2CH 720P IP Camera 8CH 1080P IP Camera 8CH 720P IP Camera |
|  | Simultaneous Remote Viewers | 6 Users Online |
| Others | Operating Temperature | 0°C ~ 55°C |
|  | Operating Humidity | 10% ~ 90% |
|  | Dimension | 330*250*55mm |
|  | Weight | 2.10 KGS |
|  | USB Mouse | YES |
|  | HDD Screw | 8 PCS (1 Pack) – 2 x HDD |
|  | Quick Start Guide (QSG) | YES |
|  | Power Supply | DC12V/4A Switching Power Adapter (included Power Cord) |
|  | Package | 5pcs/ctn (457 x 455 x 308mm/carton) |

# Text boxes

4-CH 720P AHD DVR